## Slide 1: EV4-vvvf Drive Signalling
Dr. K. Ferhat Celik
Blain Hydraulics
ferhat.celik@blain.de

## Slide 2
Temp. sensor
OPEN loop control
EV4
A practical solution for Green Hydraulic Lift applications
YASKAWA
L1000H
EV4
EV4 Valve
Motor
Pump
Lift controller
DOWN travel : Conventional (mechanical)
UP travel with inverter

## Slide 3
Power supply
12V to 35V dc
A1
Connecting the temperature converter
L1000H
Temperature Sensor
1 2 3
4 5 6
AC
+
-
Temperature Converter
Temperature sensor is dipped into the oil.

## Slide 4
Full speed travel S1+S4
Intermediate full sp travel S1+S5
Inspection speed travel S1+S6
Leveling speed travel S1
Stop
switch
Decel.
switch
Input
common
Energy to motor contactors
S4 – Speed selection signal
S1 – Up run signal
1
2
3
Stop
switch
Decel.
switch
1
2
Elevator speed
Output frequency
Signaling from lift controller
Travel signals
Base block signal
L1000H
S1 is up travel signal, without S1 elevator will not move.
S4, S5 and S6 are speed selection signals, without these elevator will move with levelling speed.
When more than one speed selection signals are used the lowest speed selection is exucuted.